## Slide 1: Hardware Connection based Serial Communication
trongnhanle@hcmut.edu.vn
trongnhanle85@gmail.com
LÊ TRỌNG NHÂN

## Slide 2: What is Serial Communication?
Serial communication is a communication method that uses one or two transmission lines to send and receive data, and that data is continuously sent and received one bit at a time.
All programmable devices have at least one serial: PC, Smartphone, Tablets, Arduino Boards

## Slide 3: Part 1: Send Commands To Hardware

## Slide 4: Step 1: Install pyserial
pip install pyserial
print("Sensors and Actuators") import time import serial.tools.list_ports

## Slide 5: Step 2: Open the port
In windows: check the port name in Device Manager/Ports
In MAC/Linux: ls /dev/tty*
try: ser = serial.Serial(port=“COMx”, baudrate=115200) except: print("Can not open the port")

## Slide 6: Step 3: Send A Command
def sendCommand(cmd): ser.write(cmd.encode())

## Slide 7: Step 4: Testing the Program
while True: print("Testing commands") sendCommand("2") time.sleep(2) sendCommand("3") time.sleep(2) sendCommand("4") time.sleep(2) sendCommand("5") time.sleep(2)
Command | Device
2 | Turn on LED
3 | Turn off LED
4 | Turn on Relay
5 | Turn of Relay

## Slide 8: Full program
print("Sensors and Actuators") import time import serial.tools.list_ports try: ser = serial.Serial(port="COM8", baudrate=115200) except: print("Can not open the port") def sendCommand(cmd): ser.write(cmd.encode()) while True: print("Testing commands") sendCommand("2") time.sleep(2) sendCommand("3") time.sleep(2) sendCommand("4") time.sleep(2) sendCommand("5") time.sleep(2)

## Slide 9: Part 2: Receive Sensory Data

## Slide 10: Receive and Process Data
mess = ""
def processData(data):
data = data.replace("!", "")
data = data.replace("#", "")
splitData = data.split(":")
print(splitData)
def readSerial():
bytesToRead = ser.inWaiting()
if (bytesToRead > 0):
global mess
mess = mess + ser.read(bytesToRead).decode("UTF-8")
while ("#" in mess) and ("!" in mess):
start = mess.find("!")
end = mess.find("#")
processData(mess[start:end + 1])
if (end == len(mess)):
mess = ""
else:
mess = mess[end+1:]

## Slide 11: Request Sensory Data
def requestData(cmd): sendCommand(cmd) time.sleep(1) readSerial()

## Slide 12: Testing the Program
while True: requestData("0") time.sleep(2) requestData("1") time.sleep(2)

## Slide 13: Exercise 1
Implement the callback message() in mqtt, in order to control a device when mqtt data is received (button on the dashboard is clicked)

## Slide 14: Exercise 2
Modify the while True in mqtt.py, in order to request the data from sensor and publish it to the mqtt server

## Slide 15: Finalize the LAB
Update your repository in Github