## Slide 1: Multi-Displicine Project based Internet of Things and Artificial Intelligence
trongnhanle@hcmut.edu.vn
trongnhanle85@gmail.com
LÊ TRỌNG NHÂN

## Slide 2: Industrial 4.0 Architecture
Proposed by Timothy Chou

## Slide 3: Project Block Function
Simple Sensors (Temperature and Humidity) and Actuators (Pump and LEDs)
AI Camera based on Google Teachable Machine
IoT Server for Remote monitoring and Controlling (Adafruit IO)
Dashboard (Website or Mobile App)
Data Analytics or ChatBot

## Slide 4: Smart Agriculture
Temperature and Humidity
pH, EC
Light intensity
Pump controllers

## Slide 5: Monitoring System based AR/VR

## Slide 6: Project Introduction
AI inference using webcam (2p)
Remote monitoring through IoTs service (4p)
Simple hardware devices (supported Hardware Abstraction Layer) (2p)
Data analytics or ChatBot (2p)
Extra features (maximum 2p)
Group of 5 – 7 students

## Slide 7: Generic AI and IoTs Architecture
Slave #1
Slave #2
Slave #40
…
Touch Screen LCD

## Slide 8: Sensors and Actuators
Physical hardware of the project
Control by RS485 connection:
  Python program sends a command
  Data is response in an array (8 bytes)

## Slide 9: Google Teachable Machine for AI
Classification — The output variable is a category, such as “red” or “blue” or “disease” or “no disease”

## Slide 10: Training the Model
More options can be changed in the Advanced

## Slide 11: Export the Model
Tensorflow – Keras and Download my model

## Slide 12: IoT Server using Adafruit IO
Free server with 60 messages/min
Support MQTT Pub/Sub, HTTP, HTTPs
Email for the Alarms

## Slide 13: Dashboard for Remote Monitoring
Web or Mobile version is encouraged
Dashboard on Adafruit IO is an option

## Slide 14: Data Analytics
Growing degree days (GDD) is a weather-based indicator for assessing crop development.
It is a function of many sensors: light, humidity, v.v…
A simple function is proposed for this feature
GDD is published to the IoT server as an additional information (or an advanced sensor)

## Slide 15: ChatBot
Rasa Framework
ChatGPT???
Voice activation controller

## Slide 16: Extra functions
Proposed by students:
  Data predictions for weather forecast

## Slide 17: Project Plan
Project Functions | Week No
Build an AI Model | 1
Adafruit IO Server | 2
Data analytics and ChatBot | 3
Simple sensors and actuator | 4
Project Proposal and Analytics | 5
Project Implementation and Integration | 6-7
Project Presentation | 8
Extra manual (Android app) | 6-7

## Slide 18: Software Requirements
Python Interpreter (version 3.8.5)
Python Editor (Pycharm or VS Code)
Github
https://zalo.me/g/ktiqwa611

## Slide 19: Exercise 1
Create a repository for your group
Create a project in python:
  adafruit-io
  tensorflow
  keras
  Pillow
  opencv-python
  pyserial